## Slide 1: Exercise: Extending Heap Allocators for CHERI
📖 Exercise 7: Extending Heap Allocators for CHERI 👩‍💻!

## Slide 2: Exercise: Extending Heap Allocators for CHERI Introduction 1
CHERI's architectural protection is driven by software -- the compiler, linker, OS kernel, run-time linker, run-time libraries, and so on all manage capabilities as part of their program execution
Heap allocators, which are integrally tied into our notions of spatial and temporal safety, are typically extended to use CHERI in five ways:
    To implement spatial safety, bounds and permissions are set on returned pointers. (In this exercise.)
    To prevent bounds overlap on larger allocations from arising due to imprecise bounds caused by capability compression, large allocations are aligned and padded more strongly. (Not in this exercise.)
    If the allocator's free() implementation relies on reaching allocator metadata via its pointer argument, then the implementation must be changed as access will otherwise be prevented by CHERI bounds and monotonicity. (In this exercise.)
    To implement temporal safety, allocated memory is registered with a temporal-safety run-time library when allocated, to implement kernel-assisted revocation. On free, the memory is is held in quarantine until revocation has been performed. (Not in this exercise.)
    To handle a further set of classes of misuse and pointer corruption, it is also important to perform validation of arguments to free(), such as by checking that the pointer is to the first byte of a valid allocation. (Not in this exercise.)

## Slide 3: Exercise: Extending Heap Allocators for CHERI Introduction 2
This exercise asks you to extend a simplified memory allocator with CHERI focusing only on (1) and (3) above
  1. To implement spatial safety, bounds and permissions are set on returned pointers
  3. If the allocator's free() implementation relies on reaching allocator metadata via its pointer argument, then the implementation must be changed as access will otherwise be prevented by CHERI bounds and monotonicity
It supports only small fixed-size allocations that will not require further alignment or padding, and we will not consider temporal safety in this exercise

## Slide 4: Exercise: Extending Heap Allocators for CHERI Introducing Heap Allocator Bounds
main() allocates memory, and then overflows the allocation to corrupt internal allocator metadata, leading to a crash.
Heap metadata corruption is a powerful exploitation tool; CHERI assists with mitigating it through pointer integrity features, but it is preferable to deterministically close vulnerabilities (e.g., via spatial safety).
Compile cheri-allocator.c with the CHERI-enabled allocator-cheri make target. Run the binary, which will crash.
Use GDB to demonstrate to yourself that the overflow has corrupted allocator metadata, leading to an eventual crash during a later call to alloc_allocate().
Program received signal SIGPROT, CHERI protection violation.
Capability tag fault caused by register ca0.
alloc_allocate () at cheri-allocator.c:83
83 alloc_nextfree = alloc->a_next;
(gdb) p alloc

## Slide 5: Exercise: Extending Heap Allocators for CHERI Set Bounds
Modify the allocator to use the cheri_bounds_set() API to set suitable bounds on the pointer returned by alloc_allocate(). Recompile cheri-allocator.c with a CHERI-enabled target.
Use GDB to demonstrate to yourself that the overflow operation now causes an immediate crash as a result of attempting to store out of bounds, rather than triggering a later crash due to heap metadata corruption.
#ifdef __CHERI_PURE_CAPABILITY__
return (cheri_bounds_set(<pointer>, <size>));
#else
return (<pointer>);
#endif
Program received signal SIGPROT, CHERI protection violation.
Capability bounds fault caused by register ca3.

## Slide 6: Exercise: Extending Heap Allocators for CHERI Reaching Allocator Metadata
Remove the overflow (performed with memset()) from the program. Recompile cheri-allocator.c with the CHERI-enabled make target.
Use GDB to explore why the program now crashes in alloc_free(): How did adding bounds during allocation break later freeing of that memory?
Correct the bug through the use of the cheri_address_get() and cheri_address_set() APIs, which allow transferring an address from one capability (with one set of bounds) to another (with a different set of bounds). What capability should we be using to provide the new bounds? Recompile cheri-allocator.c with the CHERI-enabled make target.
Demonstrate that the program now runs successfully to completion.
(gdb) bt
#0 alloc_free (ptr=<optimized out>) at cheri-allocator.c:106
#1 main () at cheri-allocator.c:137
(gdb) p alloc

## Slide 7: Exercise: Adapt a C Program to CHERI C Discussion
Where and how would we worry about alignment? Can this be avoided?
Where would we need to do extra work for temporal safety?
What properties might we validate on Free()?